ENVIRONMENTAL INSPECTION ACCORDING TO ART. 32 OF LAW ON INSPECTION SUPERVISION

# INSTALLATION: name, A/B IPPC code, town, location

# CHECKLIST – NON/ROUTINARY/CONTROL INSPECTION

# A/B-IPPC PERMIT NUMBER XXXXX

# Issued on xxxx, according to the Law of Environment (part XII)

IMPORTANT PRELIMINARY INFORMATION:

The following checklist is a template that can be used by inspectors to prepare their own checklist during the preparation of the inspection to an end-of-life vehicle (ELV) depollution & shredder plant. The Best Available Techniques (BATs) which have been included in this template belong mainly to the BAT Reference Document (BREF) for Waste treatment (draft 1, December 2015). If a BAT is mentioned in the template which does not belong to that BREF, the name of the corresponding BREF is provided.

The other BREF mentioned is on Waste Treatment Industries. See more information about this BREF documents and this kind of installations in the Factsheet for the ELV sector prepared by the Twinning project supporting SEI, which is available in SEI’s website, http://www.sei.gov.mk , in the section “Documents & links”.

This template of checklist is meant to provide a structure for a homogeneous definition of inspection checklists.

The present checklist includes the following boxes, providing examples of relevant topics to be checked:

GENERAL DATA

General elements of management

Communication duties

SECTORIAL TOPICS

Air emissions

Soil and groundwater

Waste

Energy consumption and efficiency

LIST OF POLLUTANTS TO BE ASSESSED

# GENERAL DATA

| Date of Inspection |  |
| --- | --- |
| Type of Inspection | ( Routinary ( Non Routinary ( Control (follow-up) |
| Field of inspection | ( Integrated (all environmental impacts checked) ( Partial (specify laws checked) |
| Name of Company |  |
| Location of the plant |  |
| Legal address |  |
| Industrial activity | End-of-live-vehicles (ELV) |
| Permit (number, date and title) |  |
| Permit holder |  |
| Telephone |  |
| E-mail |  |
| Contact person for integrated permit-related issues |  |
| Representative competent authority |  |

ADMINISTRATIVE ORGANISATION / INTERNAL CONTROL

| TOPIC: GENERAL ELEMENTS OF MANAGEMENT |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Presentation of the current state of the plant by the operator by means of layout and drawings |  | BREF: Waste treatment industries BAT 24b (p. 518) | Check whether any modification of the plant occurred which has not been authorized. Check the drainage infrastructure and whether it is connected with the overall drainage system of the installation. Check the whole storage area: covered, paved grounds, security signs etc. Inspect the whole area where the removed batteries are kept: pavement of the ground, avoidance of leakages etc. Inspect the whole area where ELV are stored (before dismantling): pavement of the ground Inspect the area where the removed tyres are kept: tyres must be regularly removed (fire danger!). Are there any fire extinguishers? |  |
| Environmental Management System (EMS) |  | BREF Waste treatment (draft) BAT 1 (p.882) | Check the implementation of a structured EMS. In case the installation is EMAS or ISO14001, check validity of the certificate. Interview with operator to assess the application of the procedures. Check whether the proposed EMS contains specific procedures for material flow analysis consistency of records kept about the material flow in all production units reporting procedure: who is the data manager in the facility, which authority is responsible to receive the data records |  |
| Training of personnel |  | Foreseen in the EMS | Check the existence and execution of a Training Plan on environmental topics (relevant to the installation). |  |
| Management of accidents/incidents |  |  | Check how incidents have been managed: procedures in place, register of events, follow-up actions to repair/correct: Fire extinguishers placed everywhere in the plant? Security signs in storage areas of hazardous wastes? Frequent removal of tyres? Sealed barrels/tanks of collected fluids? |  |
| Register of Maintenance |  | Foreseen in the EMS | Check the presence of a Register where the operator takes note of maintenance services occurred in the plant. |  |
| Register of Certificate of Destruction (CoD) |  |  | Check whether the register of incoming ELV (in de-pollution facilities) corresponds to the issued CoD (No of incoming ELV = issued CoD). Light fluctuations possible (10-15% less CoD than incoming ELV ) due to the fact that CoD are usually issued after a few days of ELV arrival in the de-pollution facility |  |
| xxxx |  |  |  |  |

| TOPIC: COMMUNICATION DUTIES |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Self-monitoring report |  | Foreseen in the EMS | Check the correct delivery to the Competent Authority of the self-monitoring report. Check results of the monitoring. |  |
| Incidents/Emission Limit Values |  |  | Check if the operator communicates incidents and exceedances of emission limit values to the competent authority. |  |
| Installation changes |  |  | Check that the operator asked for authorization for making changes to the installation, as specified in legislation. |  |
| xxxx |  |  |  |  |
| xxxx |  |  |  |  |
| xxxx |  |  |  |  |
| xxxx |  |  |  |  |

SECTORIAL TOPICS

| TOPIC: AIR EMISSIONS |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Pollution abatement systems |  |  |  |  |
| Pollution abatement systems (shredder) |  |  | Concentration and quantity of contaminants before and after the treatment. Duration of operation daily/annually (h) |  |
| Air emission continuous monitoring (shredder) |  |  | Check the programme of maintenance and calibration of the air emission measurements equipment |  |
| Sampling points (shredder) |  |  | Check correctness of sampling points according to EU standards |  |
| Dust (shredder) |  | BREF Waste treatment (draft) BAT 25 (p. 904) | Check which type of dust collection devices (cyclone, wet scrubber, fabric filter) is applied Check what is happening with the collected dust (e.g. transport to landfill?). |  |
| Odour |  |  |  |  |
| Greenhouse gases (de-pollution facility) |  |  | Check whether Freon storage tanks are properly sealed |  |
| xxxx |  |  |  |  |

| TOPIC: NOISE AND VIBRATION |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Noise |  |  |  |  |
| xxxx |  |  |  |  |

| TOPIC: WASTE WATER |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Pollution abatement systems (de-pollution facility) |  |  | Check the drainage infrastructure and whether it is connected with the overall drainage system of the installation: Is it connected to the municipal wastewater treatment plant? |  |
| Water use conservation measures |  |  |  |  |

| TOPIC: SOIL AND GROUNDWATER |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Leakages from storage area (de-pollution facility) |  |  | Check the whole storage area: covered, paved grounds, security signs etc. Inspect the whole area where the removed batteries are kept: pavement of the ground, avoidance of leakages etc. Inspect the whole area where ELV are stored (before dismantling): pavement of the ground |  |
| Rainwater |  | (BREF “Common Waste Water and Waste Gas Treatment/ Management Systems in the Chemical Sector”) Process water should be segregated from rainwater and other water effluent, to allow reuse or recycling, as well as to minimise the amount of waste water which requires treatment, the installation of a roof over certain process areas, loading and unloading bays, etc. Prevention of uncontrolled effluents from the site, such as contaminated rainwater. Rainwater from production areas is collected either in sumps on the spot or in other central facilities (e.g. emergency storage tanks or lagoons) to allow inspection and then a decision is to be made on whether to discharge it directly to the receiving water or to a waste water treatment facility. | Existence of systems to separate and treat first flush rainwater from later rainfall |  |

| TOPIC: WASTE |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Collection/Storage (de-pollution facility) |  |  | Check all storage devices (tanks, barrels etc.): are all removed materials properly stored (in sealed barrels/tanks ?) |  |
| Waste generated (de-pollution facility |  |  | Waste classification (according to national list of waste) EWC category: 13 01 01* hydraulic oils, containing PCBs 13 01 04* chlorinated emulsions 13 01 05* non-chlorinated emulsions 13 01 09* mineral-based chlorinated hydraulic oils 13 01 10* mineral based non-chlorinated hydraulic oils 13 01 11* synthetic hydraulic oils 13 01 12* readily biodegradable hydraulic oils 13 01 13* other hydraulic oils 13 02 04* mineral-based chlorinated engine, gear and lubricating oils 13 02 05* mineral-based non-chlorinated engine, gear and lubricating oils 13 02 06* synthetic engine, gear and lubricating oils 13 02 07* readily biodegradable engine, gear and lubricating oils 13 02 08* other engine, gear and lubricating oils 16 01 07* oil filters 16 01 08* components containing mercury 16 01 09* components containing PCBs 16 01 10* explosive components (e.g. air bags) 16 01 11* brake pads containing asbestos 16 01 12 brake pads other than those mentioned in 16 01 11 16 01 13* brake fluids 16 01 14* antifreeze fluids containing dangerous substances 16 01 15 antifreeze fluids other than those mentioned in 16 01 14 16 01 16 tanks for liquefied gas 16 01 17 ferrous metal 16 01 18 non-ferrous metal 16 01 19 plastic 16 01 20 glass 16 01 21* hazardous components other than those mentioned in 16 01 07 to 16 01 11 and 16 01 13 and 16 01 14 16 01 22 components not otherwise specified 16 01 99 wastes not otherwise specified 16 06 01* lead batteries 16 08 01 spent catalysts containing gold, silver, rhenium, rhodium, palladium, iridium or platinum (except 16 08 07) 16 08 02* spent catalysts containing dangerous transition metals (3) or dangerous transition metal compounds 16 08 03 spent catalysts containing transition metals or transition metal compounds not otherwise specified Check the records (kept by the operator) concerning the quantity of each waste/by-product (kg/day) |  |
| Disposal/recycling |  |  | Check the disposal/recycling route: Disposal (textile items): Are they disposed of in municipal landfill? Recycling ((batteries + tyres): Are they transported to other facilities for re-use/ recycling? Hazardous wastes (see above): Are they transported to hazardous waste treatment facilities (abroad)? Are the transport documents (e.g. consignment notes) for each item in consistency to the quantities transported? |  |

| TOPIC: ENERGY CONSUMPTION/EFFICIENCY (Shredder) |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
|  |  | BREF Waste treatment (draft) BAT 28 (p. 905) | Check how often the mill is shut down (register of operation/ maintenance) |  |

LIST OF POLLUTANTS TO BE ASSESSED

| Air emission pollutants | Waste water pollutants |
| --- | --- |
| SO2 Χ | Organohalogen compounds |
| Other S compounds | Organophosphorus compounds |
| NOx Χ | Organotin compounds |
| Other N compounds | Substances / mixtures possessing carcinogenic/mutagenic properties |
| CO | Persistent hydrocarbons and persistent and bioaccumulable organic toxic substances |
| VOC Χ | CN |
| Metals Χ | Metals |
| Metals compounds Χ | Metals compounds |
| Fine particulate matter Χ | As |
| Asbestos suspended particulates | As compounds |
| Asbestos fibres | Biocides |
| Cl | Suspended solids |
| Cl compounds | Nitrates |
| F | Phosphates |
| F compounds | BOD5 |
| As | COD |
| As compounds |  |
| CN |  |
| Substances / mixtures possessing carcinogenic/ mutagenic properties |  |
| Polychlorinated dibenzodioxins |  |
| Polychlorinated dibenzofurans |  |

# Footnotes

Define the kind and code of industrial activity according to the Annex I and II of the Ordinance 89/05

This list is not meant to be exhaustive; it lists common pollutants that it is usually worth to detect. Pollutants relevant to this sector are marked (X)