ENVIRONMENTAL INSPECTION ACCORDING TO ART. 32 OF LAW ON INSPECTION SUPERVISION

# INSTALLATION: name, A/B IPPC code, town, location

# CHECKLIST – NON/ROUTINARY/CONTROL INSPECTION

# A/B-IPPC PERMIT NUMBER XXXXX

# Issued on xxxx, according to the Law of Environment (part XII)

IMPORTANT PRELIMINARY INFORMATION:

The following checklist is a template that can be used by inspectors to prepare their own checklist during the preparation of the inspection to Large Combustion Plant (LCP). The Best Available Techniques (BATs) which have been included in this template belong mainly to the BAT Reference Document (BREF) for Large Combustion Plants. If a BAT is mentioned in the template which does not belong to that BREF, the name of the corresponding BREF is provided. The other BREF mentioned is the BREF on Emissions from Storage.

See more information about these BREF documents and this kind of installations in the Factsheet for Large Combustion Plants prepared by the Twinning project supporting SEI, which is available in SEI’s website, http://www.sei.gov.mk , in the section “Documents & links”.

This template of checklist is meant to provide a structure for a homogeneous definition of inspection checklists.

The present checklist includes the following boxes, providing examples of relevant topics to be checked:

GENERAL DATA

General elements of management

Communication duties

SECTORIAL TOPICS

Air emissions

Noise and vibration

Waste water

Soil and groundwater

Waste

LIST OF POLLUTANTS TO BE ASSESSED

DATA TO BE COLLECTED ACCORDING TO ART. 72 OF DIRECTIVE ON INDUSTRIAL EMISSIONS (IED)

# GENERAL DATA

| Date of Inspection |  |
| --- | --- |
| Type of Inspection | ( Routinary ( Non Routinary ( Control (follow-up) |
| Field of inspection | ( Integrated (all environmental impacts checked) ( Partial (specify laws checked) |
| Name of Company |  |
| Location of the plant |  |
| Legal address |  |
| Industrial activity | Large Combustion Plant |
| Permit (number, date and title) |  |
| Permit holder |  |
| Telephone |  |
| E-mail |  |
| Contact person for integrated permit-related issues |  |
| Representative competent authority |  |

ADMINISTRATIVE ORGANISATION / INTERNAL CONTROL

| TOPIC: GENERAL ELEMENTS OF MANAGEMENT |
| --- |
| Topic | What does the permit /National law says | What do the BREFs say/which BAT are applicable | What to check | What has been observed |
| Presentation of the present state of the plant by the operator by means of layout and drawings |  | No specific obligations in the BREF | Check whether any modifications of the plant occurred which have not been authorized. Check areas of storage and emission points. |  |
| Environmental Management System (EMS) |  | BAT 1 gives 10 criteria of the EMS to be checked | Check the implementation of a structured EMS. In case the installation is EMAS or ISO14001, check validity of the certificate. Interview with operator to assess the application of the procedures |  |
| Training of personnel |  | See BAT 1 under iv b (EMS) | Check the existence of an internal Training Plan |  |
| Management of accidents/incidents |  | No specific obligations in the BREF. In Macedonia the (EU) Seveso II Directive is applied | Check how incidents have been managed: existing of procedures, register of events, preparing follow up actions |  |
| Maintenance registers |  | See BAT 1 iv under g (EMS) | Implementation and performance of maintenance procedures |  |
| Self-ignition of fuel |  | See BAT 1 under x (EMS) | Identify risk points for fuels subject to self- ignition and survey accordingly the fuel storage areas |  |
| General environmental and combustion performance |  | BAT 4 a to g | Check if (one of a combination of) the techniques that are mentioned in the BAT are applicable for the combustion installation and in use |  |
| Energy Efficiency |  | BAT 7 a to t (20 techniques) | Check if (one or a combination) of the techniques that are mentioned in the BAT are applicable for the combustion installation and in use |  |
| Fuel characterization |  | BAT 5 | Check if the fuel composition is properly analyzed |  |
| Diffuse emissions (See air emissions) |  |  |  |  |

| TOPIC: COMMUNICATION DUTIES |
| --- |
| Topic | What does the permit /National law says | What do the BREFs say/which BAT are applicable | What to check | What has been observed |
| Self monitoring report |  | BAT 1 under v (EMS) and BAT 2 | Check the correct transmission of the self monitoring report by the operator. Check results of the monitoring. |  |
| Incidents/ELV |  | BAT 1 iv under c (EMS) | Check if the operator communicates incidents and exceedance of ELVs to the competent authority |  |
| Installation changes |  | No specific obligations in the BREF | Check that the operator asked for authorization of changes in the installation |  |

SECTORIAL TOPICS

| TOPIC: AIR EMISSIONS |
| --- |
| Topic | What does the permit /National law says | What do the BREFs say/which BAT are applicable | What to check | What has been observed |
| Pollution abatement systems solid fuels |  | BAT 17 and 18 | Check use of combustion techniques like air-and fuel staging, advanced low NOx burners etc. and check lignite pre-drying and energy performance level |  |
| Pollution abatement system solid fuels |  | BAT 19, 20, 21, 22, 23 | Check, if applicable, the use of (one of a combination of) the emission reduction techniques mentioned in the BATs for the different substances and check emission levels |  |
| Pollution abatement system liquid fuels |  | BAT 31, 35 and 40 | Check the use of one (or a combination of) the described techniques in the BATs to enhance the energy efficiency and check the energy efficiency level HFO and LFO fired boilers, HFO fired engines, LFO fired gas turbines |  |
| Pollution abatement system liquid fuels |  | BAT 32, 33, 34, 36, 37, 38, 39, 41, 42 and 43 | Check the use of one (or a combination of) the emission reducing techniques that are mentioned in the BATs for the different substances and check emission levels |  |
| Pollution abatement systems gaseous fuels |  | BAT 44 and 45 | Check, if applicable, the use of (one of a combination of) the techniques to increase the energy efficiency and check energy performance level |  |
| Pollution abatement systems gaseous fuels |  | BAT 46, 47, 48, 49, 50 | Check, if applicable, the use of (one of a combination of) the emission reduction techniques that are mentioned in the BATs for the different substances and check emission levels |  |
| Pollution abatement systems gaseous fuels (iron and steel process gases) |  | BAT 51 | Check the use of one (or a combination of) the techniques to increase the energy efficiency when combusting iron-and steel process gases and check the energy performance level |  |
| Pollution abatement systems gaseous fuels (iron and steel process gases) |  | BAT 52, 53, 54, 55, 56, 57 and 58 | Check, if applicable, the use of one (or a combination of) the emission reduction techniques that are mentioned in the BATs for the different substances and check the emission levels |  |
| Pollution abatement systems multifuel-fired plants (chemical industry process fuels) |  | BAT 62 and 63 | Check the use of the techniques to increase the environmental performance. Check fuel treatment, fuel analysis and the presence of an advanced computerized control system |  |
| Pollution abatement systems multifuel-fired plants (chemical industry process fuels) |  | BAT 64 | Check presence of heat recovery by cogeneration and energy performance level |  |
| Pollution abatement systems multi-fired plants (chemical industry process fuels) |  | BAT 65 , 66,67,69 69 | Check, if applicable, the use of (one or a combination of) the emission reduction techniques that are mentioned in the BATs for the different substances and check the emission levels |  |
| Pollution abatement systems for waste co-incineration |  | BAT 70 | Check the use of the combination of techniques to ensure stable combustion conditions and to reduce emissions to air |  |
| Pollution abatement systems for waste co-incineration |  | BAT 71 | Check the use of techniques to reduce diffuse odor emissions from the storage and handling of waste |  |
| Pollution abatement systems for waste co-incineration |  | BAT 72 | Check the minimization of the influence of waste co-incineration on the quality of by-products like gypsum, ashes and slag |  |
| Pollution abatement systems for waste co-incineration |  | BAT 73 | Check if one (or a combination of) the techniques described in BATs 7, 18, 24, 25 and 82 is used to increase the energy-efficiency |  |
| Pollution abatement systems for waste co-incineration |  | BAT 74, 75, 76, 77, 78, 79, 80, 81 | Check, if applicable, the use of one (or a combination of) the emission reduction techniques that are mentioned in the BATs for the different substances and check the emission levels |  |
| Pollution abatement systems for diffuse emissions |  | BAT 8 and 9 | Check if one (or a combination of) the techniques to reduce VOC emissions and diffuse emissions from unloading, storage and handling of fuel and additives is used |  |
| Air emission continuous monitoring |  | BAT 1 v under a and BAT 3 | Check the program of maintenance and calibration of the air emission measurements equipment and check the monitoring frequency |  |
| Sampling points |  | BAT 3 | Check correctness of sampling points according to EU standards |  |
| Dust |  | BATs 22, 29, 34, 39, 43, 58, 67,78, 85 and chapter 10.8.5 | If not yet checked before in the Pollution abatement systems, check the appropriate emission reduction technique depending on the fuel and the equipment used |  |
| Odour |  | BAT 8,9 and 71 | Check, if applicable, the use of odor emission reducing techniques from BAT 9 and from the related BATs of the BREF for Waste Treatment installations |  |
| Greenhouse gases |  | No specific obligations in the BREF as GHG are not covered by the Industrial emission directive but by the EU Emission Trading System | Presence of CO2 emission inventory |  |
| Minimize start- up and shutdown periods |  | BAT 6 | Check if policy to minimize Start-up and shutdown period is present |  |

| TOPIC: NOISE AND VIBRATION |
| --- |
| Topic | What does the permit /National law says | What do the BREFs say/which BAT are applicable | What to check | What has been observed |
| Reduction of noise emissions from relevant sources in combustion plants like boiler soot blowers, hammer mills, pneumatic transport to the burner |  | BAT 14 a to i | Check if one or a combination of the measures and techniques that are mentioned in the BAT is used and if application of these prevention techniques is adequate to maintain an acceptable noise level |  |

| TOPIC: WASTE WATER |
| --- |
| Topic | What does the permit /National law says | What do the BREFs say/which BAT are applicable | What to check | What has been observed |
| Reduction of water consumption and the volume of contaminated water discharged into receiving waters |  | BAT 10 a to d | Check if the use of potable water is avoided, if contaminated water streams are segregated, internal water recycling is maximized and if non-contaminated water streams are segregated/reused |  |
| Pollution abatement systems for water emissions |  | BAT 11 a to c | Check if mechanical treatment and /or physico-chemical treatment is applied or if there is zero liquid discharge Check the reporting on BAT-AELs and monitoring frequency according to table 10.1 of BAT 11 |  |

| TOPIC: SOIL AND GROUNDWATER |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Rainwater |  | (BREF “Common Waste Water and Waste Gas Treatment/ Management Systems in the Chemical Sector”) Process water should be segregated from rainwater and other water effluent, to allow reuse or recycling, as well as to minimise the amount of waste water which requires treatment, the installation of a roof over certain process areas, loading and unloading bays, etc. Prevention of uncontrolled effluents from the site, such as contaminated rainwater. Rainwater from production areas is collected either in sumps on the spot or in other central facilities (e.g. emergency storage tanks or lagoons) to allow inspection and then a decision is to be made on whether to discharge it directly to the receiving water or to a waste water treatment facility. | Existence of systems to separate and treat first flush rainwater from later rainfall |  |
| Tank bunds |  | (BREF “Emissions from Storage”) Design a tank farm bund (or dike) to contain large spills, such as that caused by a shell rupture or a large overfill. The bund consists of a wall around the outside of the tank (or tanks) to contain any product in the unlikely event of a spill personnel both on and off-site. The volume is normally sized to accommodate the contents of the largest tank within the bund. | Presence of tank bunds to contain spills from storage tanks and drums of waste, to prevent soil contamination in case of leakage. |  |

| TOPIC: WASTE |
| --- |
| Topic | What does the permit /National law says | What do the BREFs say/which BAT are applicable | What to check | What has been observed |
| Waste generated |  | BAT 3 and BAT 12 | Check if there is a waste management plan that ensures that waste is (in priority) avoided, reused, recycled, recovered or safely disposed of. Check if there is a waste classification (according to EWC) Quantity (kg/day) Hazardous / non-hazardous Disposal / Recycling (according to Annex I + II of the Waste Framework Directive) |  |
| Waste and residues management Reduction of waste sent for disposal |  | BAT 13 | Check if the operation on the site is organized to maximize, in order of priority: the proportion of residues that arise as by products, waste reuse according to the specifically requested quality criteria, waste recycling and other criteria by implementing on site and/or off site technical measures such as described in BAT 13 e to h for the different by products |  |
| Storage |  | BAT 9 under j; BREF Emissions from Storage | Check if air treatment of sewage sludge storage is necessary and applicable. See remark below table BAT 9 |  |
| Decommissioning |  | BAT 16 | Check if design considerations for end-of-life plant decommissioning have been established according to BAT 16 under a and b. (organizational and technical precaution measures) |  |

DATA TO BE COLLECTED ACCORDING TO ART. 72 OF DIRECTIVE ON INDUSTRIAL EMISSIONS (IED)

| Data | Unit of measure | Value |
| --- | --- | --- |
| Total rated thermal input of the combustion plant | MW |  |
| Type of combustion plant:boiler, gas turbine, gas engine, diesel engine, other | (specifying the type) |  |
| Date of the start of operation of the combustion plant | date |  |
| Total annual emissions of sulphur dioxide | (tonnes per year) |  |
| Total annual emissions of nitrogen oxides | (tonnes per year) |  |
| Total annual emissions of dust | (tonnes per year) |  |
| Number of operating hours of the combustion plant | hours |  |
| Total annual amount of energy input, related to the net calorific value broken down in terms of the following categories of fuel: coal, lignite, biomass, peat, other solid fuels (specifying the type), liquid fuels, natural gas, other gases (specifying the type). | (TJ per year), |  |
| The sulphur content of the indigenous solid fuel used | % |  |
| Rate of desulphurisation achieved, averaged over each month2 | % |  |
| Technical justification of the non-feasibility of complying with the emission limit values2 |  |  |
| The number of operating hours per year. | hours |  |

LIST OF POLLUTANTS TO BE ASSESSED

| Air emission pollutants | Waste water pollutants |
| --- | --- |
| SO2 X | Organohalogen compounds |
| Other S compounds | Organophosphorus compounds |
| NOx X | Organotin compounds |
| Other N compounds | Substances / mixtures possessing carcinogenic/mutagenic properties |
| CO X | Persistent hydrocarbons and persistent and bio accumulative organic toxic substances |
| VOC X | CN |
| Metals | Metals X |
| Metals compounds X | Metals compounds X |
| Fine particulate matter X | As X |
| Asbestos suspended particulates | As compounds X |
| Asbestos fibres | Biocides |
| Cl | Suspended solids X |
| Cl compounds X | Nitrates X |
| F | Phosphates |
| F compounds X | BOD5 X |
| As | COD X |
| As compounds |  |
| CN |  |
| Substances / mixtures possessing carcinogenic/ mutagenic properties |  |
| Polychlorinated dibenzodioxins X |  |
| Polychlorinated dibenzofurans X |  |

This is not an exhaustive list. Pollutants that are relevant for Large Combustion Plants are marked X

# Footnotes

Define the kind and code of industrial activity according to the Annex I and II of the Ordinance 89/05

For combustion plants to which Article 31 of the IED Directive applies

For combustion plants which do not operate more than 1 500 operating hours per year as a rolling average over a period of 5 years