ENVIRONMENTAL INSPECTION ACCORDING TO ART. 32 OF LAW ON INSPECTION SUPERVISION

# INSTALLATION: name, A/B IPPC code, town, location

# CHECKLIST – NON/ROUTINARY/CONTROL INSPECTION

# A/B-IPPC PERMIT NUMBER XXXXX

# Issued on xxxx, according to the Law of Environment (part XII)

IMPORTANT PRELIMINARY INFORMATION:

The following checklist is a template that can be used by inspectors to prepare their own checklist during the preparation of the inspection to a pig or poultry farm. The Best Available Techniques (BATs) which have been included in this template belong mainly to the BAT Reference Document (BREF) for Intensive Rearing of Poultry and Pigs. If a BAT is mentioned in the template which does not belong to that BREF, the name of the corresponding BREF is provided.

The other BREFs mentioned are the Reference Document on Best Available Techniques for Emissions from Storage (EFS BREF) and the Reference Document on Best Available Techniques for Waste Treatments Installations (WT BREF). See more information about these BREF documents and this kind of installations in the Factsheet for farms for intensive rearing of poultry and pigs prepared by the Twinning project supporting SEI, which is available in SEI’s website, http://www.sei.gov.mk , in the section “Documents & links”.

This template of checklist is meant to provide a structure for a homogeneous definition of inspection checklists.

The present checklist includes the following boxes, providing examples of relevant topics to be checked:

GENERAL DATA

General elements of management

Communication duties

SECTORIAL TOPICS

Air emissions

Noise and vibration

Waste water

Soil and groundwater

Waste

LIST OF POLLUTANTS TO BE ASSESSED

# GENERAL DATA

| Date of Inspection |  |
| --- | --- |
| Type of Inspection | ( Routinary ( Non Routinary ( Control (follow-up) |
| Field of inspection | ( Integrated (all environmental impacts checked) ( Partial (specify laws checked) |
| Name of Company |  |
| Location of the plant |  |
| Legal address |  |
| Industrial activity |  |
| Permit (number, date and title) |  |
| Permit holder |  |
| Telephone |  |
| E-mail |  |
| Contact person for integrated permit-related issues |  |
| Representative competent authority |  |

ADMINISTRATIVE ORGANISATION / INTERNAL CONTROL

| TOPIC: GENERAL ELEMENTS OF MANAGEMENT |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Presentation of the current state of the plant by the operator by means of layout and drawings |  | No specific obligations in the BREF | Check whether any modification of the plant occurred which has not been authorized. Check areas of storage and emission points. |  |
| Environmental Management System (EMS) |  | BAT 1 gives 11 features of the EMS to be checked. Specifically feature 10 (implementation of a noise management plant (see BAT 9) and feature 11 (implementation of a odour management plant (see BAT 12) are included for the intensive poultry or pig rearing sector | Check the implementation of a structured EMS. In case the installation is EMAS or ISO14001, check validity of the certificate. Interview with operator to assess the application of the procedures. |  |
| Training of personnel |  | See BAT 1 under 4 (b) (EMS) See BAT 2 under b | Check that the EMS includes feature 4 (b) of BAT 1 Check the existence of an internal Training Plan on environmental topics (relevant to the installation) |  |
| Management of accidents/incidents |  | See BAT 1 under 4 (h) and 5 (b) (EMS) See BAT 2 under c In Macedonia the (EU) Seveso II Directive is applied | Check that the EMS includes features 4(h)and 5(b) of BAT 1 Check the existence of an emergency plan Check how accidents/incidents have been managed: procedures in place, register of events, follow-up actions to correct/prevent |  |
| Maintenance programmes and registers |  | See BAT 1 under 4 (g) (EMS) See BAT 2 under d | Check the existence of maintenance programmes and registers where the operator takes note of maintenance services occurred in the plant. |  |
| Nutritional management |  | See BAT 3 in order to reduce the total nitrogen excreted and consequently ammonia emissions See BAT 4 in order to reduce the total phosphorous excreted | Check if the diet formulation and nutritional strategy includes one or a combination of the techniques given in table 5.1 (page 729) for BAT 3 and in table 5.2 (page 730) for BAT 4. One of the techniques mentioned is: b. Multiphase feeding with a diet formulation adapted to the specific requirements of the production period |  |
| Number of incoming and outgoing animals, including births and deaths when relevant |  | See BAT 29 under d | Check that the number of incoming and outgoing animals, including births and deaths when relevant is monitored at least once a year. Check records of existing registers |  |
| Feed consumption |  | See BAT 29 under e | Check that feed consumption is monitored at least once a year. Check records of invoices or existing registers |  |
| Manure generation |  | See BAT 29 under f | Check that manure generation is monitored at least once a year. Check records of existing registers |  |
| Energy consumption and efficiency |  | See BAT 8 in order to use energy efficiently | Check if a combination of the techniques given in the BAT are used. Two of the techniques mentioned are: a. High efficiency heating/cooling and ventilation systems c. Insulation of the walls, floors and/or ceilings of animal houses |  |
| Energy consumption and efficiency |  | See BAT 29 under b (Electric energy consumption) and c (fuel consumption) | Check if the electric energy consumption and fuel consumption are monitored at least once a year Check records of suitable meters or invoices |  |
| Water use efficiency |  | See BAT 5 in order to use water efficiently | Check if a combination of the techniques given in the BAT are used. Two of the techniques mentioned are: c. Use high-pressure cleaners for cleaning animal housing and equipment d. Select suitable equipment (e.g. nipple drinkers, round drinkers, water troughs) for the specific animal category while ensuring water availability (ad libitum) |  |
| Water use efficiency |  | See BAT 29 under a | Check if the water consumption is monitored at least once a year Check records of suitable meters or invoices |  |
| Liquid storage: soil and watercourses protection around tanks |  | No specific obligations in BREF See pages 265/267 of BREF on Emissions from Storage (EFS BREF) | Check which secondary containment measures has been applied by operator (double wall tanks, monitored bottom discharge, liquid-tight reservoir that contain all or a part of the hazardous liquids stored etc) to aboveground and underground tanks containing flammable liquids or liquids which pose a risk for significant soil pollution or a significant pollution of adjacent watercourses. |  |
| Storage of packaged dangerous substances |  | No specific obligations in BREF See page 267 of EFS BREF | Check that packaged dangerous substances are stored in a building and/or an outdoor storage area covered with a roof |  |
| Storage of solids |  | No specific obligations in BREF See page 274 of EFS BREF | Check that materials likely to produce dust (e.g. feed) are stored by using, for example, silos, bunkers, hoppers and containers, to eliminate the influence of wind and to prevent the formation of dust by wind. |  |

| TOPIC: COMMUNICATION DUTIES |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Self-monitoring report |  | See BAT 1 under 5 (a) and (c) (EMS) | Check the correct delivery to the Competent Authority of the self-monitoring report. Check results of the monitoring. |  |
| Self-monitoring report |  | See BAT 24 | Check that the total nitrogen and the total phosphorous excreted in manure is monitored at least once a year for each animal category using one of the techniques given in the BAT. One of the techniques given is b. Estimation by using manure analysis for total nitrogen and total phosphorous content |  |
| Self-monitoring report |  | See BAT 25 | Check that ammonia emissions to air are monitored using one of the techniques and at least with the frequency given in the BAT. The frequency is once a year for each animal category or every time there are significant changes to the type of livestock reared or the housing system. One of the techniques given is: c. Estimation by using emission factors |  |
| Self-monitoring report |  | See BAT 26 | Check that odour emissions are periodically monitored using the standards given in the BAT |  |
| Self-monitoring report |  | See BAT 27 | Check that dust emissions are monitored using one of the techniques in the BAT at least once a year. One of the techniques given is: b. Estimation by using emission factors |  |
| Self-monitoring report |  | See BAT 28 | Check that the ammonia, dust and/or odour emissions from an animal house equipped with an air cleaning system are monitored using one of the techniques and at least with the frequency given in the BAT. |  |
| Incidents/Emission Limit Values (ELVs) |  | See BAT 1 under 4 (c) (EMS) | Check if the operator communicates incidents and exceedances of ELVs to the competent authority |  |
| Installation changes |  | See BAT 1 under 4 (c) (EMS) | Check that the operator asked for authorization for making changes to the installation, as specified in legislation. |  |

SECTORIAL TOPICS

| TOPIC: AIR EMISSIONS |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Reduction of emissions of nitrogen, phosphorous, odour and microbial pathogens |  | See BAT 19 | Check the use of (one or a combination of) techniques given in the BAT to reduce the emission of nitrogen, phosphorous, odour and microbial pathogens to air and water from the on farm processing of manure One of the techniques given is: a. Mechanical separation of slurry |  |
| Reduction of ammonia emissions |  | See BAT 14 | Check the use of (one or a combination of) techniques given in the BAT for the reduction of ammonia emissions from the storage of solid manure One of the techniques given is: b. Cover solid manure heaps |  |
| Reduction of ammonia emissions |  | See BAT 16 | Check the use of (one or a combination of) techniques given in the BAT for the reduction of ammonia emissions from a slurry tank One of the techniques given is: b. Cover slurry tanks |  |
| Reduction of ammonia emissions |  | See BAT 17 | Check the use of (one or a combination of) techniques given in the BAT for the reduction of ammonia emissions from an earth-banked storage (lagoon) of slurry One of the techniques given is: a. Minimize stirring of the slurry |  |
| Reduction of ammonia emissions |  | See BAT 21 (application of slurry to land) | Check the use of (one or a combination of) techniques given in the BAT for the reduction of ammonia emissions from the application of slurry to land One of the techniques given is: c. Shallow injector (open slot) |  |
| Reduction of ammonia emissions |  | See BAT 22 (application of manure to land) | Check that in order to reduce ammonia emissions from the application of manure to land, manure is incorporated to soil as soon as possible either by ploughing or using other cultivation equipment. The BAT associated time delay between landspreading of manure and incorporation into the soil is 0-4 hours. The upper end of the range can be up to12 hours when conditions are not favourable for faster incorporation |  |
| Reduction of ammonia emissions |  | See BAT 23 | Check that the reduction of ammonia emissions from the whole production process is estimated/calculated using the BAT implemented on the farm |  |
| Reduction of ammonia emissions Pollution abatement systems ammonia emissions (pigs) |  | See BAT 30 | Check the use of (one or a combination of) techniques given in the BAT for the reduction of ammonia emissions from an animal house One of the techniques given is: c. Use of an air cleaning system such as wet acid scrubber, two-stage or three-stage air cleaning system or bioscrubber BAT-AEL are given in Table 5.4 (page 749) |  |
| Reduction of ammonia emissions Pollution abatement systems ammonia emissions (poultry) |  | See BAT 31 (for laying hens, broiler breeders or pullets) See BAT 32 (for broilers) See BAT 33 (for ducks) See BAT 34 (for turkeys) | Check the use of (one or a combination of) techniques given in the BAT for the reduction of ammonia emissions from an animal house One of the techniques given is: -Use of an air cleaning system such as wet acid scrubber, two-stage or three-stage air cleaning system or bioscrubber BAT-AEL are given in Table 5.5 (page 751) for laying hens and in Table 5.6 (page 751) for broilers |  |
| Air emission continuous monitoring |  | See BAT 1 under 5 (a) (EMS) | Check the programme of maintenance and calibration of the air emission measurements equipment and check the monitoring frequency |  |
| Sampling points |  | No specific obligations in the BREF | Check correctness of sampling points according to EU standards when applicable (e.g. stacks of boilers for heating systems) |  |
| Dust |  | See BAT 11 | Check the use of (one or a combination of) techniques given in the BAT for the reduction of dust emissions from an animal house One of the techniques given is: c. Treatment of exhaust gas by an air cleaning system such as: water trap, dry filter, water scrubber, wet acid scrubber, bioscrubber (or biotrickling filter) two-stage or three-stage air cleaning system or biofilter |  |
| Odour |  | See BAT 13 See BAT 12 See BAT 1 under 11 (EMS) | Check the use of a combination of the techniques given in the BAT for the prevention or, where that is not practicable, for the reduction of odour emissions from an animal house (BAT 13) One of the techniques given is: d. Use an air cleaning system such as: bioscrubber (or biotrickling filter), biofilter or two-stage or three-stage air cleaning system Check the existence and implementations of an odour management plan (BAT 12) |  |
| Greenhouse gases |  | No specific obligations in the BREF as GHG are not covered by the Industrial Emissions Directive but by the EU Emission Trading System See BAT 8 in order to use energy efficiently | Check if a combination of the techniques given in the BAT are used. |  |

| TOPIC: NOISE AND VIBRATION |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Noise |  | See BAT 10 See BAT 9 See BAT 1 under 10 (EMS) | Check the use of a combination of the techniques given in the BAT for the prevention or, where that is not practicable, for the reduction of noise emissions (BAT 10) Two of the techniques given are: b. Equipment location: increase the distance between the emitter and the receiver; minimise the length of feed delivery pipes; locate the feed bins and fee silos so as to minimise the movement of vehicles in the farm e. Noise-control equipment which includes: noise reducers; vibration isolation; enclosure of noisy equipment (e.g. mills, pneumatic conveyers); soundproofing of buildings Check the existence and implementation of a noise management plan (BAT 9) |  |

| TOPIC: WASTE WATER |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Reduction of waste water generation |  | See BAT 6 | Check the use of a combination of techniques given in the BAT in order to reduce the generation of waste water. Two of the techniques given are: a. Keep the fouled yard areas as small as possible. c. Segregate uncontaminated rainwater from waste water streams that require treatment. |  |
| Reduction of waste water emission to water Pollution abatement systems for water emissions |  | See BAT 7 | Check the use of (one or a combination of) techniques given in the BAT in order to reduce emissions to water from waste water. Two of the techniques given are: a. Drain waste water to a dedicated container or to a slurry store. b. Treat waste water. |  |
| Reduction of emissions to water |  | See BAT 15 | Check the use of a combination of techniques given in the BAT in order to prevent, or where that is not practicable, to reduce emissions to soil and water from the storage of solid manure. Two of the techniques given are: b. Use a concrete silo for storage. d. Select a storage facility with a sufficient capacity to hold manure during periods in which the application to land is not possible. |  |
| Prevent emissions to water |  | See BAT 18 | Check the use of a combination of techniques given in the BAT in order to prevent emissions to soil and water from from slurry collection, piping and from a tank and/or an earth-banked storage (lagoon). Two of the techniques given are: b. Select a storage facility with a sufficient capacity to hold manure during periods in which the application to land is not possible. e. Install a leakage detection system. |  |
| Reduction of emissions of nitrogen, phosphorous, odour and microbial pathogens to water |  | See BAT 19 | Check the use of (one or a combination of) techniques given in the BAT to reduce the emission of nitrogen, phosphorous, odour and microbial pathogens to air and water from the on farm processing of manure Two of the techniques given are: a. Mechanical separation of slurry b. Anaerobic digestion of manure in a biogas installation. |  |
| Reduction of emissions of nitrogen, phosphorous, odour and microbial pathogens to water |  | See BAT 20 | Check the use of all of the techniques given in the BAT to reduce the emission of nitrogen, phosphorous, odour and microbial pathogens to soil and water from the spreading of manure to land Techniques a, b, c, d, e, f, g and h are given. Accordingly, check the existence and implementation of a Plan for manure spreading which includes the techniques given and in which all the plots of arable land where the manure will be spread are identified. |  |

| TOPIC: SOIL AND GROUNDWATER |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Reduction of emissions to soil |  | See BAT 15 | Check the use of a combination of techniques given in the BAT in order to prevent, or where that is not practicable, to reduce emissions to soil and water from the storage of solid manure. Two of the techniques given are: b. Use a concrete silo for storage. d. Select a storage facility with a sufficient capacity to hold manure during periods in which the application to land is not possible. |  |
| Prevent emissions to soil |  | See BAT 18 | Check the use of a combination of techniques given in the BAT in order to prevent emissions to soil and water from from slurry collection, piping and from a tank and/or an earth-banked storage (lagoon). Two of the techniques given are: b. Select a storage facility with a sufficient capacity to hold manure during periods in which the application to land is not possible. e. Install a leakage detection system. |  |
| Reduction of emissions of nitrogen, phosphorous, odour and microbial pathogens to soil |  | See BAT 20 | Check the use of all of the techniques given in the BAT to reduce the emission of nitrogen, phosphorous, odour and microbial pathogens to soil and water from the spreading of manure to land Techniques a, b, c, d, e, f, g and h are given. Accordingly, check the existence and implementation of a Plan for manure spreading which includes the techniques given and in which all the plots of arable land where the manure will be spread are identified. |  |
| Rainwater |  | (BREF “Common Waste Water and Waste Gas Treatment/ Management Systems in the Chemical Sector”) Process water should be segregated from rainwater and other water effluent, to allow reuse or recycling, as well as to minimise the amount of waste water which requires treatment, the installation of a roof over certain process areas, loading and unloading bays, etc. Prevention of uncontrolled effluents from the site, such as contaminated rainwater. Rainwater from production areas is collected either in sumps on the spot or in other central facilities (e.g. emergency storage tanks or lagoons) to allow inspection and then a decision is to be made on whether to discharge it directly to the receiving water or to a waste water treatment facility. | Existence of systems to separate and treat first flush rainwater from later rainfall |  |

| TOPIC: WASTE |
| --- |
| Topic | What does the permit /National law say | What do the BREFs say | What to check | What has been observed |
| Storage of dead animals |  | See BAT 2 under e | Check the use of all the techniques given in the BAT in order to prevent or reduce the environmental impact and improve the overall performance. The following technique is included: e. Store dead animals in such a way to prevent or reduce emissions |  |
| Waste generated |  | No specific obligations in the BREF See BAT 57 of BREF document for the Waste Treatment Industries (WT BREF) | Check if there is a waste management plan that ensures that waste is (in priority) avoided, reused, recycled, recovered or safely disposed of. Check if there is a waste classification (according to EWC) Quantity (kg/day) Hazardous / non-hazardous Disposal / Recycling (according to Annex I + II of the Waste Framework Directive) |  |
| Waste management and storage |  | No specific obligations in the BREF See BAT 58 of WT BREF See BAT 59 of WT BREF | Check that the use of re-usable packaging is maximized (BAT 58 of WT BREF) Check that drums (to collect waste) are re-used when they are in a good working state and that in other cases, they are sent for appropriate treatment (BAT 59 of WT BREF) |  |
| Hazardous waste collection and storage |  | No specific obligations in the BREF | Check that hazardous wastes are collected and stored separately and are not mixed among them or with non-hazardous waste or other substances and materials. Check that they are kept secure so they do not leak, spill, or blow away and with compliance with the regulations. Check that they are transferred, accompanied by the supporting documents to an authorised waste management company. |  |

LIST OF POLLUTANTS TO BE ASSESSED

| Air emission pollutants | Waste water pollutants |
| --- | --- |
| SO2 | Organohalogen compounds |
| Other S compounds | Organophosphorus compounds |
| NOx X | Organotin compounds |
| NH3 X | Substances / mixtures possessing carcinogenic/mutagenic properties |
| N2O X | Persistent hydrocarbons and persistent and bioaccumulable organic toxic substances X |
| CO X | CN |
| CO2 X | Metals (Cu,Zn, Pb) X |
| CH4 X | Metals compounds |
| VOC | As |
| Metals | As compounds |
| Metals compounds | Biocides |
| Fine particulate matter X | Suspended solids X |
| Asbestos suspended particulates | Nitrates X |
| Asbestos fibres | Phosphates X |
| Cl | BOD5 X |
| Cl compounds | COD X |
| F |  |
| F compounds |  |
| As |  |
| As compounds |  |
| CN |  |
| Substances / mixtures possessing carcinogenic/ mutagenic properties |  |
| Polychlorinated dibenzodioxins |  |
| Polychlorinated dibenzofurans |  |

# Footnotes

Define the kind and code of industrial activity according to the Annex I and II of the Ordinance 89/05

This list is not meant to be exhaustive; it lists common pollutants that it is usually worth to detect.