ENVIRONMENTAL INSPECTION ACCORDING TO ART. 32 OF LAW ON INSPECTION SUPERVISION

# INSTALLATION: name, A/B IPPC code, town, location

# CHECKLIST – HORIZONTAL BREFs & BAT INSPECTION

# A/B-IPPC PERMIT NUMBER XXXXX

# Issued on xxxx, according to the Law of Environment (part XII)

PURPOSE OF THIS DOCUMENT:

The aim of this document is to cover a set of topics to be checked during an inspection, applicable to the majority of IED plants. It can be both used as a tool during the preparation phase and during the inspection visit.

It is recommended that, when preparing the inspection and checking the permit and other relevant documents, the inspector goes through this document, selecting those parts which are relevant to the installation to be inspected, and includes them in the general checklist template that complements this document, as part of the preparation of his/her own checklist (he/she will have to add as well other aspects specific to the permit, kind of installation, or installation itself).

One added value of such a checklist is to give the opportunity to the inspector to become more familiar with BAT Reference Documents (BREFs), in order to be able to go through those documents and have a better knowledge of BAT (Best Available Techniques); the increased comprehension of processes allows the inspector to be more active when suggesting permit improvements to the permit writer and when discussing with the operator about BAT applicability.

The following checklist focuses on some of the general requirements (most of them BATs) included in “vertical” (sectorial) BREFs, and in the following “horizontal” BREFs (applicable to many different kinds of installations):

- Energy efficiency (February 2009)

- Common waste water and waste gas treatment / management systems in the chemical sector (February 2003)

- Emissions from storage (July 2006)

- JRC Reference document on Monitoring of Emissions from IED installations. (October 2013)

The checklist is not considered to be exhaustive of the above mentioned BREFs’ contents. The present checklist includes the following boxes:

- General data

- Topic 1: Storage and handling

- Topic 2: Emissions from storage

- Topic 3: Energy efficiency

- Topic 4: Common waste water and waste gas treatment / management systems in the chemical sector

- Topic 5: Monitoring

- Topic 6: Environmental management system

- Topic 7: Resource management

- Topic 8: Check of adequate BAT process management

GENERAL DATA

| Date of Inspection |  |
| --- | --- |
| Type of Inspection | ( Routinary ( Non Routinary ( Control (follow-up) |
| Field of inspection | ( Integrated (all environmental impacts checked) ( Partial (specify laws checked) |
| Name of Company |  |
| Location of the plant |  |
| Legal address |  |
| Industrial activity |  |
| Permit (number, date and title) |  |
| Permit holder |  |
| Telephone |  |
| E-mail |  |
| Contact person for integrated permit-related issues |  |
| Representative competent authority |  |

HORIZONTAL TOPICS

| TOPIC 1: STORAGE AND HANDLING |
| --- |
| Ref. to the BREF | Topic | BAT | What to check | What has been observed |
| BREF: Waste treatment industries BAT n.24 b) Pag.518 | Storage and handling | Ensuring that the storage area drainage infrastructure can contain all possible contaminated run-off and that drainage from incompatible wastes cannot come into contact with each other | Check the separation among wastes with different properties; check if rainwater can produce a leakage of the waste; check the drainage infrastructure. Check whether any hazardous wastes are stored properly (safety regulations) |  |
| BREF: Waste treatment industries BAT n.48 Pag.521 | Storage and handling | Collect the rainwater in a special basin for checking, treatment if contaminated and further use. | Check the separation among wastes with different properties; check if rainwater can produce a leakage of the waste. |  |
| BREF: Waste treatment industries BAT n.24 d) Pag.518 | Storage and handling | Handling odorous materials in fully enclosed or suitably abated vessels and storing them in enclosed buildings connected to abatement. | Check from the yearly report the presence of odorous wastes; check how they are stored. |  |
| BREF: Waste treatment industries BAT n.24 g) Pag.519 | Storage and handling | Equipping tanks and vessels with suitable abatement systems when volatile emissions may be generated, together with level meters and alarms. | Check from the yearly report the presence of waste that can produce volatile emissions; check how they are stored and the presence of abatement systems. |  |
| BREF: Waste treatment industries BAT n.57 Pag.522 | Storage and handling | Have a waste management plan | Check if they have procedures to manage existing waste streams; check if they maximize the re-use of generated waste (i.e. separation of waste streams, transport to waste recycling centers) |  |
| BREF: Production of Cement, Lime and Magnesium Oxide | Emissions from storage | BATs 13, 14 and 15 | Applied BATs and other measures prescribed in permit |  |
| BREF: Iron and Steel Production | Emissions from storage | BATs 6,7,8,9,10 and 11 | Applied BATs and other measures prescribed in permit |  |
| BREF: Non ferrous metals industries | Emissions from storage | BATs 6 and 7 (table in BAT 7) | Applied BATs and other measures prescribed in permit |  |
| BREF: Intensive rearing of poultry and pigs | Emissions from storage | BATs 2,3,8,9,27,28,29 and 44 | Applied BATs and other measures prescribed in permit |  |
| BREF: Ceramics | Emissions from storage | BATs stated under ch.5.1.3.1b P205 See also ch. 4.2.2 | Applied BATs and other measures prescribed in permit |  |
| BREF: Common Waste Water and Waste Gas Treatment | Emissions from storage | BATs 9 and 21 | Applied BATs and other measures prescribed in permit |  |
| BREF: Ferrous metals processing | Emissions from storage | No general BATs for prevention of emission from storage | Eventual prescriptions in permit (e.g.good housekeeping) |  |

| TOPIC 2: BREF “EMISSIONS FROM STORAGE” (JULY 2006) |
| --- |
| Ref. to the BREF: EMISSIONS FROM STORAGE | Topic | BAT | What to check | What has been observed |
| Pag. 265/267 | Liquid storage: soil protection around tanks | Provide secondary containment to aboveground and underground tanks containing flammable liquids or liquids that pose a risk for significant soil pollution or a significant pollution of adjacent watercourses. Install a liquid-tight reservoir that can contain all or a part of the dangerous liquids stored. | Check which secondary containment measures has been applied by operator (double wall tanks, monitored bottom discharge, etc). |  |
| Pag. 267 | Storage of packaged dangerous substances | Apply a storage building and/or an outdoor storage area covered with a roof. | Check where dangerous substances are stored. |  |
| Pag. 270 | Transfer and handling of liquids and liquefied gases | For large storage facilities, according to the properties of the products stored, BAT is to apply a leak detection and repair programme. | Check if the operator as a leak detection and repair programme. |  |
| Pag. 274 | Storage of solids | BAT is to apply enclosed storage by using, for example, silos, bunkers, hoppers and containers, to eliminate the influence of wind and to prevent the formation of dust by wind. | Check the storage areas of materials likely producing dust. |  |
| Pag. 274 | Open storage of solids | BAT for open storage are: moistening the surface covering the surface solidification of the surface grassing-over of the surface | Check the measures undertaken by the operator for the avoidance of dust release (e.g. coverage of storage areas) |  |

| TOPIC 3: BREF “ENERGY EFFICIENCY” (FEBRUARY 2009) |
| --- |
| Ref. to the BREF: ENERGY EFFICIENCY | Topic | BAT | What to check | What has been observed |
| BREF Energy efficiency n.3-4 Pag.275 | Energy efficiency | Identify the aspects of an installation that influence energy efficiency by carrying out an audit | Check if the operator ever performed an audit. Check the content of the audit: - energy-using equipment, and the type and quantity of energy used in the installation; - detected possibilities to minimise energy use and to avoid energy losses - possibilities to use alternative sources or use of energy that is more efficient. |  |
| BREF Energy efficiency n.8 Pag.277 | Energy efficiency | Establish energy efficiency indicators | Check if the operator identified suitable energy efficiency indicators for the installation, and measure their change over time or after the implementation of energy efficiency measures |  |
| BREF Energy efficiency n.15 Pag.281 | Energy efficiency | Carry out maintenance at installations to optimise energy efficiency. | Check if the operator applies the following: establishing a structured programme for maintenance supporting the maintenance programme by appropriate record keeping systems and diagnostic testing |  |

| TOPIC 4: BREF “COMMON WASTE WATER AND WASTE GAS TREATMENT / MANAGEMENT SYSTEMS IN THE CHEMICAL SECTOR” (FEBRUARY 2003) |
| --- |
| Ref. to the BREF: COMMON WASTE… | Topic | BAT | What to check | What has been observed |
|  | Waste water assessment | Checking and identifying relevant water-consuming processes and listing them according to their water usage. The resultant ranking is the basis for improvement of water consumption | Check whether any wastewater/ cooling water recirculation systems are applicable. |  |
| Pag. 275 | Waste water and waste gas treatments | Treat contaminated waste water/waste gas streams at source in preference to dispersion and subsequent central treatment. | Check if the operator treats or pre-treats the effluents (water, gas) at source (not using a centralized treatment plant). |  |
| Pag. 276 | Waste water | Using process water in a recycle mode whenever feasible for economic and quality reasons. | Check if the process foresees recycling measures of the process water. |  |
| Pag. 277 | Waste water | Segregate process water from uncontaminated rainwater and other uncontaminated water releases. | Check if the operator takes adequate measures to avoid rainwater to mix with process water. |  |
| Pag. 279 | Rainwater | Duct uncontaminated rainwater directly to a receiving water, by-passing the waste water sewerage system. Treat rainwater from contaminated areas. | Check the discharging of rainwater and the possibility to be contaminated. Check whether any possibilities for on-site treatment and reuse of rainwater from contaminated areas can be applied. |  |
| Pag. 293 | Waste water discharge | BAT-associated emission levels for final waste water discharge into surface water | Compare the emission values of waste water discharge into surface water with BAT-associated emission levels |  |

| TOPIC 5: MONITORING |
| --- |
| Ref. to the BREF | Topic | BAT | What to check | What has been observed |
| Production of Cement, Lime and Magnesium Oxide | Monitoring | BATs 5, 32 and 55 Monitoring and measurement of process parameters and emissions to be executed in accordance with relevant EN and ISO standards | Measurement procedures (handbooks) and reporting |  |
| Iron and Steel Production | Monitoring | BAT conclusions: BATs 13,14,15 and 16 | Stack emissions whenever BAT-associated emission levels are given Direct measurements Indirect measurements Calculations |  |
| Non ferrous metals industries | Monitoring | BATs 3 and 4 Process control and emission monitoring | 11 techniques (a-k) as described in table BAT3 |  |
| Intensive rearing of poultry and pigs | Monitoring | BATs 11-17 | Mass balances and calculations on emissions Logbooks and self monitoring reports |  |
| Ceramics | Monitoring | No BATs, reference to background document on p95 | Check monitoring at specific BATs |  |
| Common Waste Water and Waste Gas treatment | Monitoring | BATs 3,4,5, and 6 | Monitoring according to the methods and standards given in the BAT (tables) |  |
| Ferrous metals processing | Monitoring | No BATs, BREF is outdated (2001) | Monitoring conditions in permit (if applicable) |  |

| TOPIC 6: ENVIRONMENTAL MANAGEMENT SYSTEM |
| --- |
| Ref. To the BREF | Topic | BAT | What to check | What has been observed |
| All BREFs | EMS | Commitment of senior management | Official company documents on the EMS |  |
| All BREFs | EMS | Establishment of environmental policy including continuous improvement of installations by management | Company documents on the EMS and most recent reporting on results |  |
| All BREFs | EMS | Planning, establishing and implemention of necessary procedures, objectives and targets in conjuction with financial planning and investment | Company documents and reports on the EMS about targets and necessary investments |  |
| All BREFs | EMS | Implementation of structure, responsibility, training, communication and documentation | Reports on results of EMS implementation in the company |  |
| All BREFs | EMS | Performance and corrective action, monitoring and measurement and preventive action | How does the system work, how is the monitoring and measurement organized |  |
| All BREFs | EMS | Maintenance of records Independent internal and external auditing | The presence of auditing reports |  |
| All BREFs | EMS | Review EMS by senior management on adequacy and effectiveness | Is a regularly review organized? |  |
| All BREFs | EMS | Following development of cleaner technologies | Presence of knowledge about new developments in the industrial sector |  |
| All BREFs | EMS | Consideration of the environmental impacts of decommisioning during design and operating life | Is relevant information on decomissioning gathered during the design and/or operating life available? |  |
| All BREFs | EMS | Application of sectoral benchmarking on a regular basis | Is the operator aware of the environmental performance of other companies in the sector? What is the knowledg about international norms and standards |  |
| All BREFs | EMS | Independent audits EMS | Is the EMS and audit procedure examined and validated by an accredited certification body or an external EMS verifier? |  |
| All BREFs | EMS | EMAS and EN-ISO 14001:1996 | Is there an implementation and adherence to an internationally accepted voluntary system such as EMAS and EN ISO 14001: 1996? |  |
| Large Combustion Plants | EMS | BAT1 sub x | Is there an identification of risk points for fuel to self-ignition and survey acordingly to the fuel storage areas |  |
| Non ferrous metals Industry | EMS | BAT 1 sub j | Is there an action plan on diffuse dust emissions? |  |
| Intensive Rearing of Pigs and Poultry | EMS | BAT 1 sub 10 and 11 | Implementation of noise- and odor action plans |  |
| Surface Treatment using Organic Solvents | EMS | BAT 13 | Choice of input materials to reduce environmental footprint |  |
| Tanning of Hides and Skins | EMS | BAT 1 sub x | Maintenance of records of the locations on the site where particular process steps are carried out |  |
| Waste incineration | EMS | BAT 56 | Preparation of a commissioning program Gap analysis of training requirements Inventory of health and safety needs Availability of up to date documentation regarding the installation Emergency and accident prevention planning |  |
| Wood based Panels Production | EMS | BAT 1 sub X to XIV | Waste management plan Quality control plan Noise management plan Odor management plan Dust management plan |  |

| TOPIC 7: RESOURCE MANAGEMENT |
| --- |
| Topic | Range/values set in the BREFs and BAT Conclusions | What has been observed | Compliance (YES/NO) |
| INPUTS |
| Main raw material (ton/day) |  |  |  |
| Chemical (additive) 1 (kg/ton of raw material) |  |  |  |
| Chemical (additive) 2 (kg/ton of raw material) |  |  |  |
| Chemical (additive) x (kg/ton of raw material) |  |  |  |
| Water (m3/day) |  |  |  |
| Energy (kWh/day) |  |  |  |
| OUTPUTS |
| Product 1 (ton/day) Product 1 (ton / ton of main raw material) |  |  |  |
| Product 2 (ton/day) Product 2 (ton / ton of main raw material) |  |  |  |
| By-product 1 (ton/day) By-product 1 (ton/ton of main raw material) |  |  |  |
| By-product 2 (ton/day) By-product 2 (ton/ton of main raw material) |  |  |  |
| By-product x (ton/day) By-product x (ton/ton of main raw material) |  |  |  |
| Air emissions | SO2 (mg/Nm3) |  |  |  |
|  | NOx (mg/Nm3) |  |  |  |
|  | xxx (mg/Nm3) |  |  |  |
|  | xxx (mg/Nm3) |  |  |  |
| Wastewater | Amount discharged (kg / ton of raw material) |  |  |  |
|  | Biochemical Oxygen Demand (BOD5) (mg/l of wastewater) |  |  |  |
|  | Chemical Oxygen Demand (COD) (mg/l of wastewater) |  |  |  |
|  | xxx |  |  |  |
| Waste | Main waste stream (kg / ton of raw material) |  |  |  |
|  | Waste stream 2 (kg / ton of raw material) |  |  |  |
|  | Waste stream 3 (kg / ton of raw material) |  |  |  |
|  | xxx |  |  |  |

| TOPIC 8: CHECK OF ADEQUATE BAT PROCESS MANAGEMENT |
| --- |
| Topic | What to check | What has been observed |
| Process design | Is the configuration of the process’ modules arranged according to the manufacturer’s instructions? |  |
|  | Have any design’s modifications occurred? If YES, for which reasons? |  |
|  | Do any improvements result from these modifications? |  |
|  | Are there any corrective measures planned to overcome any malfunctions of the process? If YES, specify the achieved improvement of the process features (in environmental terms e.g. less use of water/ energy) |  |
| Equipment | Has the equipment been installed/ operated according to its technical specifications? |  |
|  | Any changes/ modifications occurred? If YES, specify the achieved improvements |  |
|  | Is the equipment regularly checked for defects, leakages? |  |
|  | Is maintenance performed regularly according to the equipment’s specifications? |  |
| Use of resources | Are the quantities of raw materials, water, chemicals, energy introduced in the production process (inputs) according to the technical prescriptions? If NO, specify the reasons and the achieved improvements in the production process |  |
|  | Are measured/ weighted quantities of raw materials, chemicals, water registered? If NO, specify why |  |
|  | Is the least polluting energy source used for the production e.g. natural gas? If NO, specify why |  |
|  | Is the energy input measured? If NO, specify why |  |
|  | Which process outputs (products, by-products, air emissions, effluents, waste) are measured? If NO, specify why |  |
|  | How is the heating/cooling system operated? |  |
|  | Are there any special precautions to avoid losses/leakages from the feeding devices of inputs (raw materials, chemicals)? If NO, specify why |  |
|  | Are there any special precautions to avoid losses/leakages from the storage devices for raw materials/chemicals needed? If NO, specify why |  |
|  | Are there any special precautions to avoid losses/leakages from the water feeding system? If NO, specify why |  |

# Footnotes

IED = Directive 2010/75/EU on Industrial Emissions

All BREFs are available in English in http://eippcb.jrc.ec.europa.eu/reference/

The still applicable version of this reference document on monitoring dates from 2003 and is very outdated. The new version that will replace it (expected to come soon) will not be very different from the final draft of October 2013, so it is better to take this final draft as the reference in this check list. Define the kind and code of industrial activity according to the Annex I and II of the Ordinance 89/05

This table should provide a comparison between the performance data of the plant  (in terms of consumption of resources, production of waste, total emissions), with the values set in the BREFs and BAT conclusions. Therefore the unit of measure to be used should be set according to the relevant values in the BREFs and BAT conclusions.

For each product or by-product, please provide both amounts, in ton/day, and in ton/ton of main raw material.

This table provides a guidance to check if a certain BAT which is in place is properly managed or not.